FT DX 3000

New Crystal Rooﬁng Filters provide ultimate weak signal receiver

performance in crowded, strong signal environments

HF/50 MHz 100 W Transceiver

e amazing Crystal Roo ng Filter performance

has been proven in the FT DX 5000!

The Down conversion 9 MHz 1st IF frequency receiver construction, can realize

narrow 300 Hz (optional), 600 Hz and 3 kHz bandwidth rooﬁng ﬁlters.

Implementing the extra sharp Crystal Rooﬁng Filters provides superior close-in

dynamic range and affords the best receiver performance possible.

Large and wide color LCD display

The 3.5-inch wide color LCD displays the operating information and the status of

the transceiver functions, with high resolution (480 x 272 dots) on the screen.

The various FTDX3000 functions are displayed on this LCD and provide the

operator with easy to read operating information.

High Speed Spectrum Scope built-in

Although the FTDX3000 has only one receiver, a high speed Spectrum Scope is

built into the radio. When in the Auto Mode, the Spectrum Scope display is

updated in real time. The maximum bandwidth of the scope is 1 MHz, and the

minimum span width setting is 20 kHz. The best desired span is selectable for the

high resolution display. The current band activity can be monitored in real time.

AF SCOPE display and RTTY/PSK encoder/decoder (optional)

CENTER: 9 MHz

300 Hz, 600 Hz, 3 kHz Crystal roofing Filters

SPAN: 20 kHz

Characteristics of the Crystal Roofing Filter (300 Hz)

Outstanding receiver performance

is the heritage of the FT DX 5000

The essential elements in receiver performance are the RF ampliﬁer and the 1st mixer.

YAESU pursued the ultimate performance of these circuits. The RF ampliﬁer has

optimized NF points, and the over-sized wide range RF transformer exhibits minimum

saturation in strong signal processing. The optimized devices were selected to

guarantee superior multi-signal RX performance. The desired maximum performance

has been realized in the development of the

14 MHz BAND CW (BW = 500 Hz)

FTDX3000 receiver circuitry. The FTDX3000IPO ON, Roofing FILTER = 600 Hz

2 kHz Spacinghas the high dynamic range IP3 performance

-126 dBm-20 dBmIP3 : +33 dBmthat was realized and proven in the FTDX5000.

RX OUTPUT [dB]

Optional AF SCOPE and optional RTTY encoder/decoder functions have been

developed.

The wave form of the AF SCOPE signal can be displayed on the TFT LCD. Also,

the RTTY/PSK text may be displayed on the LCD.

Independent Frequency display

The Main operating frequency is the most important display in the radio, VFO-A

frequency is located just above the main dial. The newly developed LCD has a

wider viewing angle and higher contrast for convenient and effortless viewing.

Other features

• The specialized Receiver ampliﬁer for 50 MHz is built in

• Three antenna connectors are provided.

The “ANT-3” terminal may be assigned to “RX-only”

• Signal output for an external receiver and the 9 MHz IF output are furnished

• High speed Automatic antenna tuner built in

• Optional μ-tune unit available

• USB interface equipped

Rear panel view

DR : 106 dB

SIG

3rd IMD

ANT INPUT [dBm]

RF amp with the large size

wide range transformer

The 1st mixer that provides

optimum reception performance

3rd Order Dynamic Range / IP3

IF DSP provides e ective and optimized QRM rejection

The 32 bit high speed ﬂoating decimal DSP (max 2800 MIPS) provides effective

cancellation/reduction (DNR) of the random noise that is frequently frustrating in

the HF frequencies. Also: the AUTO NOTCH (DNF) that automatically eliminates

the dominant beat tone, the CONTOUR, and the APF, are very effective receiver

noise reduction tools in the HF bands operations. The YAESU original DSP QRM

and noise reduction functions are provided.

FTDX3000 Specifications

RX Frequency Range: 30 kHz - 56 MHz (operating)

1.8 MHz - 54 MHz (specified performance, Amateur bands only)

TX Frequency Ranges: 1.8 MHz - 54 MHz (Amateur bands only)

Frequency Stability: ±0.5 ppm (after 1 minute @+14 °F to +122 °F [–10 °C to +50 °C])

Operating Temperature Range: +14 °F to +122 °F (–10 °C to +50 °C)

Emission Modes: A1A (CW), A3E (AM), J3E (LSB, USB), F3E (FM),

F1B (RTTY), F1D (PACKET), F2D (PACKET)

Frequency Steps: 1/10 Hz (SSB, CW, & AM), 100 Hz (FM)

Antenna Impedance: 50 Ohms, unbalanced

16.7 - 150 Ohms, unbalanced (1.8 - 29.7 MHz)

25 - 100 Ohms, unbalanced (50 - 54 MHz)

(Tuner ON, 1.8 MHz - 50 MHz Amateur bands, TX only)

Power Consumption (Approx.): RX (no signal) 1.8 A

RX (signal present) 2.1 A

TX (100 W) 23 A

Supply Voltage: DC 13.8 V ± 10% (Negative Ground)

Dimensions (WxHxD): 14.4” x 4.5” x 12.3” (365 x 115 x 312 mm)

Weight (Approx.): 22.0 lbs (10 kg)

General

Power Output: 5 - 100 watts (2 - 25 watts AM carrier)

Modulation Types: J3E (SSB): Balanced,

A3E (AM): Low-Level (Early Stage),

F3E (FM): Variable Reactance

Maximum FM Deviation: ±5.0 kHz/ ±2.5 kHz

Harmonic Radiation: Better than -60 dB (1.8 MHz - 29.7 MHz Amateur bands: Harmonics)

Better than -50 dB (1.8 MHz - 29.7 MHz Amateur bands: Others)

Better than -65 dB (50 MHz Amateur band)

SSB Carrier Suppression: At least 60 dB below peak output

Undesired Sideband Suppression: At least 60 dB below peak output

3rd-order IMD: –31 dB @14 MHz 100 watts PEP

Bandwidth: 3 kHz (LSB/USB), 500 Hz (CW), 6 kHz (AM), 16 kHz (FM)

Audio Response (SSB): Not more than -6 dB from 300 to 2700 Hz

Microphone Impedance: 600 Ohms (200 to 10k Ohms)

Transmitter

Receiver

Circuit Type: Double-conversion Superheterodyne

Intermediate Frequencies: 9.000 MHz/ 30 kHz (24 kHz for AM/FM)

This device has not been approved by the FCC. This device may not be offered for sale or lease or be sold or leased until approval of the FCC has been obtained.

The information shown is preliminary and may be subject to change without notice or obligation.

Sensitivity: SSB (BW: 2.4 kHz, 10 dB S+N/N)

4 µV (0.5 - 1.8 MHz) (IPO “ON”)

0.16 µV (1.8 - 30 MHz) (RF AMP 2 “ON”)

0.125 µV (50 - 54 MHz) (RF AMP 2 “ON”)

AM (BW: 6 kHz, 10 dB S+N/N, 30 % modulation @400 Hz)

28 µV (0.5 - 1.8 MHz) (IPO “ON”)

2 µV (1.8 - 30 MHz) (RF AMP 2 “ON”)

1 µV (50 - 54 MHz) (RF AMP 2 “ON”)

FM (BW: 15 kHz, 12 dB SINAD)

0.5 µV (28 - 30 MHz) (RF AMP 2 “ON”)

0.35 µV (50 - 54 MHz) (RF AMP 2 “ON”)

There is no specification for frequency ranges not listed.

Selectivity (WIDTH: Center): Mode -6 dB -60 dB

CW/RTTY/PKT 0.5 kHz or better 750 Hz or less

SSB 2.4 kHz or better 3.6 kHz or less

AM 6 kHz or better 15 kHz or less

FM 15 kHz or better 25 kHz or less

Image Rejection: 70 dB or better (1.8 MHz - 30MHz Amateur bands)

60 dB or better (50 - 54MHz Amateur band)

Maximum Audio Output: 2.5 W into 4 Ohms with 10% THD

Audio Output Impedance: 4 to 8 Ohms (4 Ohms: nominal)

Conducted Radiation: Less than 4 nW

Tennozu Parkside Building

2-5-8 Higashi-Shinagawa, Shinagawa-ku, Tokyo 140-0002, Japan

YAESU MUSEN CO., LTD.

http://www.yaesu.com/jp

YAESU USA

http://www.yaesu.com

US Headquarters 6125 Phyllis Drive, Cypress, CA 90630, U.S.A.

YAESU UK http://www.yaesu.co.uk

Unit 12, Sun Valley Business Park, Winnall Close

Winchester, Hampshire, SO23 0LB, U.K.

2012.0503SS(USA/EXP/EU) B9200639 Printed in Japan

http://www.yaesu.com.hk

Unit 1306-1308, 13F., Millennium City 2, 378 Kwun Tong Road,

Kwun Tong, Kowloon, Hong Kong

YAESU HK